3rd Alpine Conference on Solid State NMR

Chamonix Mont-Blanc, FRANCE  September 14-18, 2003

POSTER#P9

DISCRETE POINT-DIPOLES WITHIN A SEMIMICRO VOLUME ELEMENT: Induced Field Contributions at the Centre and the Dependence on Shape factors

Presented at the venue by the AUTHOR:-

Sankaramapadi  ARAVAMUDHAN

Department of  Chemistry

North Eastern Hill University

SHILLONG (Meghalaya)  793022

INDIA

Hotlinks to Website Pages to View:

1.A Documentation about proceeding to Take Part in

3rd Alpine conference on SSNMR is at the Web page URL:

http://geocities.com/amudhan_nehu/3rd_Alpine_SSNMR_Aram.html

2.Results presented at the Conference get a POSTER-VIEW Documentation at the Web page URL: http://geocities.com/amudhan_nehu/Abstract_3rdalpine_SSNMR.html

3. Results presented get a SLIDE-VIEW Documentation at the web page URL:

http://geocities.com/amudhan_nehu/graphpresent.html

[A color print-out of this title page can be convenient for a prominent display on notice boards]

INTRODUCTION

Reliable HR PMR measurements made till now- in Solid-State on Single-crystal specimens for the determination of Shielding Tensor parameters which can be extracted from the experimentally measured rotation patterns, required that the specimen be of spherical shape.

If the experiments are carried out on Spherically shaped specimens, then the bulk susceptibility contributions to the Induced fields at the site of the proton become tractable which otherwise inextricably get compounded with the near-neighbourhood contributions and Intramolecular contributions to the shielding at a proton site. The near-neighbourhood contributions can be calculated-out using a magnetic dipole model and lattice summation procedure over a region of 100 A( radius from the proton site. This contribution from the spherically shaped inner semimicro volume element when calculated out and separated, then from the region outside this sphere the bulk susceptibility contribution would be zero if the macroscopic specimen outer shape is also spherical. This inner volume element which is a hypothetically carved out sphere is referred to as the Lorentz’s sphere. If the material inside the sphere can be considered as non-contributing for any reason, in such contexts this can be effectively considered as a spherical cavity.

The lattice-sum type calculations for Induced field contributions from induced magnetic dipoles within the Lorentz’ sphere is found to result in constant value for the total contribution within a radius of about 100 A( since contributions included from regions beyond this radius do not add to the total obtained for upto 100 A(. This if we may call  as a trend to converge to a limiting value for a spherical volume element, this  has not been considered in any more greater detail than simply stating that at lattice point in Cubic Crystal Lattices, this sum converges to a total of zero value.

Obviously it is the HR PMR measurements which have clearly established the importance of this convergence within the semimicro spherical volume element, identifiable  as the limiting intermolecular contributions to the Shielding tensor. Significantly this can be calculated, and corrected for, to obtain reliable intra-molecular shielding tensor values of protons in single crystals of organic molecules and similar systems.

If an ellipsoidal semimicro volume element is considered instead of the spherical element, what could be the type of convergence-trends? What consequence this would have in HR PMR measurements made and can this indicate the trends for arbitrary shapes and not only for the known regular shapes? How much can this lead to a relaxation in the stringency of the required Spherical Macroscopic specimen shape?

DIMENSION RP(20,20,20),RM(20,20,20),AGLPR(20,20,20),IL(50),

1AGLP(20,20,20),AGLM(20,20,20),SIGP(20,20,20),SIG(20,20,20),

2AGL(20,20,20),RADL(50),SIGTR(50),Y(50),IYP(50),IC(50)

DIMENSION IX(50),IB(50),GS(50),YS(50,10)

CHARACTER IX*1,IB*1,AA*1,AB*1,AC*7,AD*1,IL*1

DATA IX/50*' '/,IB/50*' '/,AA/1*'X'/,AB/1*'!'/

DATA AC/1*'-------'/,AD/1*':'/,IL/50*' '/

OPEN (5,FILE='FLEINP.INP')

OPEN (6,FILE='FLEOUT.OUT')

OPEN (7,FILE='FLEOUT2.OUT')

READ (5,60) IYSF

60  FORMAT (I2)

IYS=0

52  IYS=IYS+1

IF (IYS.EQ.IYSF) GO TO 53

READ (5,51) A,B,C

51  FORMAT (3F4.1)

READ (5,50) RLT, RLTINC, CZ, BY

50  FORMAT (F5.1,3(F4.2))

# DO 10 L=1,48

RLT=RLT-RLTINC

LL=1

SIGT=0.0

DO 2 I=1,20

DO 2 J=1,20

# DO 2 K=1,20

AIP=I

AIM=-I

BJP=J

BJM=-J

CKP=K

CKM=-K

RM(I,J,K)=SQRT((AIM*A)**2+(BJM*B)**2+(CKM*C)**2)

RP(I,J,K)=SQRT((AIP*A)**2+(BJP*B)**2+(CKP*C)**2)

PZ=CKP*C

PMZ=CKM*C

AGLPR(I,J,K)=(PZ/RP(I,J,K))

AGLP(I,J,K)=ACOS(AGLPR(I,J,K))

AGLM(I,J,K)=(PMZ/RM(I,J,K))

AGL(I,J,K)=ACOS(AGLM(I,J,K))

AGLP(I,J,K)=AGLP(I,J,K)*(180.0/3.14)

AGL(I,J,K)=AGL(I,J,K)*(180.0/3.14)

SIGP(I,J,K)=2.0*(1.0-3.0*(AGLPR(I,J,K)**2))/RP(I,J,K)**3

SIG(I,J,K)=2.0*(1.0-3.0*(AGLM(I,J,K)**2))/RM(I,J,K)**3

RLTEP=RLT*AGLPR(I,J,K)/CZ                                   C

RLTEP=RLTEP**2

AGLS=(1.0-AGLPR(I,J,K)**2)

RLTES=(AGLS*(RLT/BY)**2)

RLTE=SQRT(RLTEP+RLTES)                                                         A

IF (RP(I,J,K).GT.RLTE) GO TO 7

SIGT=SIGT+(SIGP(I,J,K)+SIG(I,J,K))

6   RLTEM=RLT*AGLM(I,J,K)/CZ                      B                      Z

RLTEM=RLTEM**2

AGLMS=(1-AGLM(I,J,K)**2)                                     Y                   X

RLTMS=(AGLMS*RLT**2)/BY**2

RLTM=SQRT(RLTMS+RLTEM)

IF (RM(I,J,K).GT.RLTM) GO TO 2

SIGT=SIGT+(SIGP(I,J,K)+SIG(I,J,K))

GO TO 2

7   GO TO 6

2   CONTINUE

RADL(L)=RLT

SIGTR(L)=SIGT

YS(L,IYS)=SIGTR(L)

10   CONTINUE

C      PRINT 3,(((RP(I,J,K),K=1,2),J=1,2),I=1,2)

C      PRINT 3,(((RP(I,J,K),K=1,3),J=1,3),I=1,3)

C      PRINT 3,(((AGLP(I,J,K),K=1,2),J=1,2),I=1,2)

C      PRINT 3,(((AGLM(I,J,K),K=1,3),J=1,3),I=1,3)

WRITE (6,44)

44  FORMAT (2X,'Lorentz Cavity Shield Calculations for Increasing',/,

12X,'Spherical/Elliptical Cavity Radius around the Nuclear Site',/,

22X,'Printed out serial number,Radius value,Induced Field Sum')

DO 14 L=1,16

14  WRITE (6,12) L,RADL(L),SIGTR(L),L+16,RADL(L+16),SIGTR(L+16),

1L+32,RADL(L+32),SIGTR(L+32)

WRITE (6,*) (' PROGRAM FOR PLOTTING, PRESS"ENTER" ')

PAUSE

YMAX=SIGTR(1)

YMIN=SIGTR(1)

DO 30 I=1,48

IF (SIGTR(I).LT.YMIN) YMIN=SIGTR(I)

30  IF (SIGTR(I).GT.YMAX) YMAX=SIGTR(I)

DO 31 I=1,48

Y(I)=SIGTR(I)-YMIN

Y(I)=Y(I)/(YMAX-YMIN)

31  IYP(I)=16.0*Y(I)+1.0

WRITE (6,*) (' NORMALISED AND INTEGERISED sum VALUES')

DO 40 I=1,16

40  WRITE (6,41) Y(I),IYP(I),Y(I+16),IYP(I+16),Y(I+32),IYP(I+32)

41  FORMAT (3(1X,E12.6,1X,I4,3X))

PAUSE

ILINE=18

34  ILINE=ILINE-1

IJ=0

DO 32 I=1,48

IF (IYP(I).EQ.ILINE) IJ=1

IF (IYP(I).EQ.ILINE)GS(ILINE)=SIGTR(I)

32  IF(IYP(I).EQ.ILINE)IX(I)=AA

IF (IJ.EQ.1) GO TO 47

WRITE (6,36) (IX(J),J=1,48)

GO TO 49

47  WRITE (6,48) GS(ILINE),(IX(J),J=1,48)

48  FORMAT (2X,E10.4,2X,48A1)

49  DO 46 I=1,48

# 46  IF(IYP(I).EQ.ILINE)IX(I)=AD

36  FORMAT (14X,48A1)

IF(ILINE.EQ.1) GO TO 35

GO TO 34

12  FORMAT (2X,3(1X,I2,1X,F5.1,1X,E10.4,2X))

3   FORMAT (3X,/,'----->>',5(2X,F8.3))

35  WRITE (6,38) AB,AC,AB,AC,AB,AC,AB,AC,AB,AC,AB,AC,AB

38  FORMAT (14X,6(A1,A7),A1)

WRITE (6,39) (RADL(I),I=1,48,8)

39  FORMAT (14X,6(F5.1,3X),'<---Radius values')

GO TO 52

53  DO 56 L=1,48

56  WRITE (7,54) L,RADL(L),(YS(L,IYS),IYS=1,IYSF-1)

54  FORMAT (I3,1X,F6.1,7(E12.5))

STOP

END

# Text boxes

A,B and C are the Lattice Constants for the three AXES in the rectangular axes system

RLT=The Maximum Radius for the inner Volume element

RTLINC=The decrement in the radius of the inner volume element for the next summation

CZ / BY = ratio determining the ellipsoidal shape factors. The ellipsoid is set to have its PRINCIPAL axes z,y, and x along the C,B and A axes. Hence from the value of RLT in any direction with a polar angle the maximum radial distance would be calculated to conform to the Ellipsoidal Shape

## A Listing of the FORTRAN

PROGRAM used for the

CALCULATIONS reported in this

POSTER presentation

(--- 4 display sheets---)

### AFTER theFortran Statement # 14 in the previous sheet, at the PAUSE Statement

the PLOT program begins which results in the plot output as in the sheets

following this PROGRAM LISTING Sheets