EUREKA CAN-displacement

Weigh specimen on scale, fill can till overflow but w/o letting overflow into cylinder, immerse object, weigh overflowed water 1g=1cm3

Weight/Volume of Displaced Water

PYCNOMETER-displacement

Weight gem in air

Weight empty bottle in scale

Fill bottle w/ water & insert stopper, reweigh

Insert gem, water overflows, reweigh

W3-W2=WA

W4-W2=WB, A-B

W1/(A-B)

SPRING BALANCE-hydrostatic

Weigh stone in Air (top pan)

Weigh stone in Water (lower pan)

Weight in Air

Weight In Air-Weight in H20

HANNEMAN BALANCE-hydrostatic

Suspend beam, lower weigh pan immersed in beaker of water, gemstone weighed in upper pan, gemstone weighed in lower pan, weight is slid towards fulcrum.  SG is read of beams calibrated scales at suspension point

TWO PAN   BALANCE

Glass beaker, platform positions beaker above one of balance pan, spiral wire stone holder suspends gem in water.  “Tare” or counterpoise, accounts for the weight of the stone holder.  All same material weight etc.  Measurements made a 4ºc

Weight in Air/Weight In Air – Weight in H20

# Text boxes

Water, Overflow Can

Wire Gauze

Ring Clamp

Support Stand

Graduated cylinder

Top Pan

Bottom pan and beaker w/ water

Fulcrum

# Zero Weight

Indicator Weights

Zero Card