## HELPFUL TIPS

- Place strap with no twists.

- Use a locking clip for continuous loop seat belts.

- Replace car seats that are over 6 years old or damaged unless otherwise stated by manufacturer.

- Check for white marks on plastic, torn padding, cracks, rust, or frayed harness.

- Adjust straps to be snug and lie flat. No more than 1 finger between the belt and the child's collarbone.

- Double back all straps.

- Check mid-ear level is not higher than the top of the back of the child seat or vehicle seat.

HOW TO USE YOUR CAR SEAT

# CAR SEAT

- Follow the instructions and keep them with the car seat. You will need them as child gets bigger.

- Send in the registration card that comes with the car seat. It will be important in the event your car seat is recalled.

# PLACEMENT

- An infant in a rear-facing seat should never be placed in the front seat of a vehicle that has a passenger-side airbag.

- Whenever possible, children should ride in the rear seat. Middle position is safest.

- If toddlers must ride in the front seat of a vehicle that has a passenger side airbag, the vehicle seat must be placed as far back as possible.

- If you use a seat made only for infants, always face it backward.

- Infants should ride facing the back of the car until they are 20 pounds and at least one year of age or until they reach the rear-facing weight limit of the seat.

- A child may face forward if they are over 20 lbs. and over one year of age.

# SECURING THE CHILD

- The shoulder straps of the car seat go in the lowest slots for infants riding backward, and the highest slots for children facing forward.

- The retainer clip should be placed at armpit level to keep harness straps on the shoulders.

  - Must be secured to vehicle with seat belt.

  - Harness straps should be snug. So snug that you cannot fit more than one finger at the child's collarbone.

- Is the auto seat belt in the right place and pulled tight?

- The belt must go to correct path to hold the seat in place

- Top must be tethered to an anchor bolt behind the seat to prevent movement in a collision or sudden stop.

- Check the owner's manual for your car to see if you need to use a locking clip or some additional piece of equipment to keep the safety seat secure.

- A convertible seat faces backward for an infant and forward for a toddler. It has two different belt paths, one for each direction.

DOES IT FIT IN YOUR CAR

- Not all car seats fit in all vehicles.

- When the car seat is installed, be sure it does not move side-to-side or toward the front of the car.

- Be sure to read the section on car seats in the owner's manual for your car.

- Is your child growing too tall for the convertible seat and are your child at least 40 pounds?

BOOSTER SEAT.

- The belt-positioning booster seat helps protect your child until he or she is big enough to use a seat belt alone.

- A booster seat with a shield must have the shield removed after the child reaches 40 lbs. and then is used with a lap and shoulder belt.

RECALL

- Call the auto safety hotline for a list of recalled seats that need repair --U.S. Department of Transportation Auto Safety Hotline, 800-424-9393.

- Designs have been modified and improved, but products continue to be recalled.

- Every safety seat made for sale in the U.S. today must be crash-tested and labeled with the name of the manufacturer, the date made, and a statement that safety seats may or may not be safe.

- Using a new car seat is safest.

- If you must use a used car seat, make sure it was never in a crash, is in good repair with no cracks, is less than ten years old and preferably less than five, and has all of its parts, including its instruction booklet.

- To check out which seats have been recalled, visit the National Highway Traffic Safety Administration web site at www.nhtsa.dot.gov.