GCE O Level Physics Just-In-Time Revision : Electricity  II

2005 Physics JIT Revision Worksheet # 7

Name : _________ Reg. No. : _____ Class : ________ Date : _______

Practice Questions

- A metal wire , 20.0 cm , with cross sectional area 5.00 mm2, has resistance 100 (. The material of this wire is used to made other wires. Determine their resistances

| Wire | Material | Length / cm | X-area / mm2 | Resistance / ( |
| --- | --- | --- | --- | --- |
| A | W | 20.0 | 5.00 | 100 |
| B | W | 20.0 | 10.0 |  |
| C | W | 40.0 | 5.00 |  |
| D | W | 60.0 | 20.0 |  |
| E | W |  | 5.00 | 200 |
| F | W | 20.0 |  | 200 |

- a) Determine the resistance of resistors that has Voltage-Current variation shown . [2]




R1 = __________

R2 = __________

b) Determine the resistance of resistors that has Voltage-Current variation shown . [2]




R3 = __________

R4 = __________

  - PQ is made of uniform high resistance wire (nichrome). Contact S can slide along PQ. PQ acts as a variable resistor. Resistance of PQ is 20 ohms. Length of PQ is 10.0 cm. 












a) Calculate the Reading on Voltmeter V1 and Ammeter A1 when PS is 0.00 cm. [2]




b) Calculate the Reading on Voltmeter V1 and Ammeter A1 when PS is 3.00 cm. [2]

  - Explain why thicker wire is used for carrying high current, and thinner wire is used for carrying lower current. [2]

  - A light bulb is short-circuited as shown.

a) Sate what happens the brightness of lamp after short-circuit. [1]


b) The lamp has 150 ( resistance. Emf of dry cell is 12.0 V. Determine the change in current due to short circuit. [2]




c) Hence, explain why short circuit is dangerous. [1]

d) Draw the current flow after the short circuit. [1]
Solutions : 
1.

| Wire | Material | Length / cm | X-area / mm2 | Resistance / ( |
| --- | --- | --- | --- | --- |
| A | W | 20.0 | 5.00 | 100 |
| B | W | 20.0 | 10.0 | 50 |
| C | W | 40.0 | 5.00 | 200 |
| D | W | 60.0 | 20.0 | 75 |
| E | W | 40.0 | 5.00 | 200 |
| F | W | 20.0 | 2.50 | 200 |

- a)R1 = 50 V / 2 A = 25.0 (
 R2 = 30 V / 4 A = 7.5 (
b) R3 = 2 V / 50 A = 0.04 (
R4 = 4 V / 30 A = 0.133 (

- a) current = 12 V / 3 ( = 4.00 A
A1 = 4.00 A ; V1 = 4.00 A x 3 ( = 12.0 V
b) current = 12 V / (3 ( + [3/10][20 (] ) = 12 V / 9  (= 1.33 A
A1 = 1.33 A ; V1 = 1.33 A x 3 ( = 4.00 V

- High current generates a lot of heat in the wires, which may cause fire or heating  damage. . Heat generated in wires = I2Rt  , where I is the current in wire, R is resistance of wire, and t is duration wire flows. To reduce the heating effects of high current, the resistance of wire R must be lowered. Thick wire, having larger cross sectional area, has lower resistance. This reduces the heating effects of the high current.

- a) Lamp goes OFF (no light) after short circuit. 
b) current before SC = 12 V / (100 ( + 150 () = 0.048 A.
current after SC = 12 V / 100 ( = 0.12 A
current change = + 0.072 A 
c) During short circuit, a high current flows in the circuit. This may cause heating damage to devices or fire.  
d)

- Answers provided by carrotisgood@hotmail.com  please visit www.geocities.com/lemonisnice for Physics notes   . ( good luck . om . . . . .

# Text boxes

P7

5 mm2

20.0 cm

Voltage / V

Current / A

0

0

50

2

4

30

Resistor R1

Resistor R2

VR1

3.00 (

P

Q

S

V1

A1

12.0 V

100 (

100 (

After Short circuit

Resistor R4

Resistor R3

30

4

2

50

0

0

Voltage / V

Current / A

After Short circuit

100 (