Super Clear Physics Revision Chart 01 ©

Try this . . .

(a) Calculate the resultant force acting on the box. [2]




(b) Hence calculate the acceleration of the box. [2]

Super Clear Physics Revision Chart 02 ©

Try this . . .

g = 10.0 N/kg

(a) Calculate the weight of a 2.00 kg box . [2]






(b) Calculate the weight of a 300 g box . [2]

Super Clear Physics Revision Chart 03 ©

Example :

Moment caused by weight of rod about pivot

= 12.0 N x 0.50 m = 6.00 Nm clockwise

Try this . . .

g = 10.0 N/kg

- Calculate the moment caused by the weight about the pivot. [2]

- Calculate the force F needed to balance the rod. [2]

Super Clear Physics Revision Chart 04 ©

Example :

Work done by 6.00 N = 6.00 N X 5.00 m = 30.0 J

Try this . . .

(a) The box moves 20.0 cm. Calculate the work done by the 13.0 N .           [2]

(b) Suppose the box moves with constant speed in a straight line. What has the work done by pushing force gone to ?                                                              [1]

Super Clear Physics Revision Chart 05 ©

Example :

A 4000 kg car is moving at speed 3.00 m/s. Calculate its kinetic energy. [2]

KE = ½ m V2 = ½ x 4000 x 3.00 m/s x 3.00 m/s = 18 000 J

Try this . . .

A ball , 40.0 g is moving at constant speed 1.10 m/s.

(a) Calculate the kinetic energy of the ball.            [2]

(b) As the ball moves up the slope, it goes slower. Neglect air resistance & friction. State the energy conversion. [1]

Super Clear Physics Revision Chart 06 ©

Example :

A 5.00 kg box is raised as shown. G = 10.0 N/kg.

Calculate gain in GPE .        [2]

Gain in GPE = m g h  = 5.00 kg x 10.0 N/kg x 1.50 m = 75.0 J

Try this . . .

A ball , 700g drops from rest from a height of 30.0 cm. 

(a) Calculate the loss in GPE .         [2]





(b) Assuming no air resistance, what happen to the loss in GPE ? [1]

Super Clear Physics Revision Chart 07 ©

Example :

A rocket accelerates at 8.00 m/s2.  Initially the rocket is at rest.  Calculate the speed of the rocket after 2.00 s. 

a = (v-u) / t ;             8.00 m/s2 = (v – 0) / 2   ;          V = 16.0 m/s

Try this . . .

A car is cruises at 12.0 m/s for 5.00s . It then accelerates at 0.500 m/s2 for 3.00s.

(a) Calculate the car’s speed after 3.00 s of acceleration. [2]






(b) Draw the velocity time graph and hence calculate total distance moved.    [3]

Super Clear Physics Revision Chart 08 ©

Example :

Calculate the potential difference across the resistor.

V = R I = 20.0 ( x 0.20 A = 4.00 V

Try this . . .

(a) Calculate the voltage (potential difference)  measured by voltmeter.         [2]




(b) Is the current flowing through the 20.0 ( resistor bigger than , smaller than   or the same as the current flowing through the 10.0 ( resistor ?                      [1]

Super Clear Physics Revision Chart 09 ©

Example :

A 50.0 W lamp operates with 230 V. Calculate the current flowing in the lamp. [2]

P = I V ; 50 W = I x 230 V ; I = 0.217 A

Try this . . .

A 2000 W oven operates with 230 V. 

(a) Calculate the current flowing in the oven.           [2]

(b) If there exist 1A, 3A, 5A, 10A and 13A fuses, which fuse is suitable for the oven ?                      [1]

(c) Calculate how much energy, in J ,  is used up by 2000 W lamp for 1.00 minute. [2]

Super Clear Physics Revision Chart 10 ©

Example :

A machine is rated 3000 W. Calculate how much energy is used in 2.00 minutes. [2]

P = E / t    ;         E = P t = 3000 W x 120 s = 360 000 J

Try this . . .

A drilling machine is rated 20.0 W.

(a) Calculate how much energy is consumed in 30.0 s.      [2]

(b) Explain why not all the input electrical energy is converted to useful output energy. [1]

Super Clear Physics Revision Chart 11 ©

Example :

Calculate the acceleration of object.          [2]

A = (v-u) / t = (6-0) / 2 = 3.00 m/s2.

Try this . . . .

Calculate the acceleration of the car.  [2]

Super Clear Physics Revision Chart 12 ©

Example :

Calculate the total distance travelled.          [2]

Distance = area of v-t graph = [  ½ x 2 x 4  ]  +   [ 3 x 4] = 14.0 m

Try this . . . .

Calculate the distance travelled when car is decelerating. [2]

# Text boxes

rF = m a

Resultant force = mass x acceleration

Example :

6.00 N = 2.00 kg x 3.00 m/s2

12.0 N

1.00 N

W = m g

weight = mass x gravitational acceleration

Example :

20.0 N = 2.00 kg x 10.0 m/s2

Weight = 12.0 N

Moment = force x  distance

50.0 cm

50.0 cm

40.0 cm

50.0 cm

Weight = 16.0 N

F

Work done = force x distance

moment = force x perpendicular distance

Work done = force x parallel distance

6.00 N

1.50 m

5.00 m

13.0 N

friction

KE  = ½ m V2

Kinetic energy = ½ x mass x speed squared

GPE  =  m g h

Gravitational potential energy

= mass x gravity acceleration x vertical height

a  =  (v-u) / t

1.50 m

5.00 m

acceleration = (final speed – initial speed) / time

V  =  R I

voltage = resistance x current

V

0.20 A

20.0 (

20.0 (

0.30 A

V

10.0 (

P  =   I  V

Power = current x voltage

P  =   En / t

Power = energy / time

G V-T   =  a

gradient of speed time graph = acceleration

V / ms-1

t / s

0

0

2

5

4

6

5

2

0

0

t / s

V / ms-1

2

5.00 kg

V / ms-1

t / s

0

0

2

5

6

V / ms-1

t / s

0

0

2

5

6

2

A V-T   =  d

area under speed time graph = distance travelled