LSGI 237

Surveying I

Tutorial Exercise: Geodetic Coordinates

Wong Wing Sum

02049440d

# Question 1.

First we define 5 points on the map provided, and then measure its X, Y coordinates on the map and calculate the N values

Readings on the map provided

| Point No. | X | Y | N |
| --- | --- | --- | --- |
| 1 | 13.4 | 11.0 | -1.64 |
| 2 | 19.6 | 12.2 | -1.00 |
| 3 | 18.2 | 5.85 | -0.85 |
| 4 | 5.5 | 4.95 | -2.00 |
| 5 | 14.9 | 13.85 | -1.63 |

We use these readings to transfer to the local coordinates system.

For example, we measure point 1’s X coordinate and Y coordinate on the map. Then measure the height by measuring the length between the point and its nearest contour and the length between two contours, then transfer them to a true local coordinate system.

Values on the map are:

X=13.4cm

Y=11.0cm

Length between the point and its nearest contour = 1.4cm

The shortest length between two contours which pass through the point = 5.1cm

Contour interval = 0.5m

We can calculate the “real world” local coordinate by

X:

1/240000 = 13.4/X

X =3216000cm

X = 32160m

Y:

1/240000 = 11.0/Y

Y = 2640000cm

Y = 26400m

Z:

0.051/0.5 = 0.014/k

k=0.137m

Z = -(1.5+ 0.137) m

Z = -1.64m

After these calculation we can have the below table

| Point No. | X | Y | N |
| --- | --- | --- | --- |
| 1 | 32160 | 26400 | -1.64 |
| 2 | 47040 | 29280 | -1.00 |
| 3 | 43680 | 14040 | -0.85 |
| 4 | 13200 | 11880 | -2.00 |
| 5 | 35760 | 33240 | -1.63 |

Afterward, we can establish the N Model

LSGI 237

Surveying I

Tutorial Exercise: Geodetic Coordinates

Wong Wing Sum

02049440d

# Question 1.

First we define 5 points on the map provided, and then measure its X, Y coordinates on the map and calculate the N values

Readings on the map provided

| Point No. | X | Y | N |
| --- | --- | --- | --- |
| 1 | 13.4 | 11.0 | -1.64 |
| 2 | 19.6 | 12.2 | -1.00 |
| 3 | 18.2 | 5.85 | -0.85 |
| 4 | 5.5 | 4.95 | -2.00 |
| 5 | 14.9 | 13.85 | -1.63 |

We use these readings to transfer to the local coordinates system.

For example, we measure point 1’s X coordinate and Y coordinate on the map. Then measure the height by measuring the length between the point and its nearest contour and the length between two contours which pass through the point, then transfer them to a “real world” local coordinate system.

Values on the map are:

X = 13.4cm

Y = 11.0cm

Length between the point and its nearest contour = 1.4cm

The shortest length between two contours which pass through the point = 5.1cm

Contour interval = 0.5m

We can calculate the “real world” local coordinate, since we have to scaling of the calculated coordinates by 1: 500, so that we have to divide the X, Y values by 500cm.

X:

1/240000 = 13.4/X

X =3216000cm

X = 32160m

X = 32160/5 = 6432m

Y:

1/240000 = 11.0/Y

Y = 2640000cm

Y = 26400m

Y = 26400/5 = 5280

Z:

0.051/0.5 = 0.014/k

k=0.137m

Z = -(1.5+ 0.137) m

Z = -1.64m

After these calculation we can have the below table

| Point No. | X | Y | N |
| --- | --- | --- | --- |
| 1 | 32160 | 26400 | -1.64 |
| 2 | 47040 | 29280 | -1.00 |
| 3 | 43680 | 14040 | -0.85 |
| 4 | 13200 | 11880 | -2.00 |
| 5 | 35760 | 33240 | -1.63 |

Afterward, we can establish the N Model