COMPOUND JOINT:

# Alternate Vector Analysis Solution

# VECTOR DIAGRAM:

# Co-ordinates of Points for Angle Calculations

# CALCULATION of ANGLES:

(mj, rj) means the dihedral angle between two planes, defined by the cross products m x j and r x j of vectors which lie on the planes of interest.

Angle between Inclined Deck and Actual Deck:

(r, - k) = 23.18011

Angles at 8/12 peaks:

(r, m) = 73.83926

(r, n) = 73.83926

Angles at Beam ends:

(r, i) = 73.83924

(r, j) = 73.83924

Vectors perpendicular to Roof planes:

j x i = - k = (0, 0, -1)

m x j = (.55470, 0, -.83205)

n x m = (.46154, .46154, -.69231)

i x n = (0, .55470, -.83205)

Vectors perpendicular to Planes of Convergence:

r x i = (0, -3.35641, -1.01624)

r x j = (3.35641, 0, 1.01624)

r x m = (-.56371, 3.35641, .84556)

r x n = (-3.35641, .56371, -.84556)

Backing Angle complements and Backing Angles:

# TRIGONOMETRIC SOLUTIONS:

# Arcos and Arcsin Forms of Equations

cos SS = cos R1 cos C5

The ji Beam plane, mj Common plane and in Common plane values may be solved using:

SS = arcos(cos 16.161 cos 16.845) = 23.180

nm Rafter plane:

SS = arcos(cos 16.161 cos 12.172) = 20.134

cos DD = sin C5 / sin SS

ji, mj, and in planes:

DD = arcos(sin 16.845 / sin 23.180) = 42.591

nm Rafter plane:

DD = arcos(sin 12.172 / sin 20.134) = 52.226

sin P2 = cos R1 cos DD

ji, mj, and in planes:

P2 = arcsin(cos 16.161 cos 42.591) = 45.000

nm Rafter plane:

P2 = arcsin(cos 16.161 cos 52.226) = 36.039

Alternate DD formulas:

sin DD = tan R1 / tan SS

tan DD = sin R1 / tan C5

Alternate P2 formulas:

cos P2 = sin R1 / sin SS

cos P2 = sin DD / cos C5

SUMMARY:

Initial calculations are as per LBN #40 article. The angles discussed are with respect to the Inclined deck.

By definition, Convergence vector r is common to all Planes of Convergence. All Ridge vectors i, j, m and n, as well as r, pass through a common point at the intercept of the ridge lines.

##### Evaluate the 90-R1 angles between the Ridge vectors and r. All R1 angles must be equal.

Taking the cross products of successive pairs of Ridge vectors yields vectors perpendicular to the Roof planes. The cross product of each Ridge vector and r produces a vector perpendicular to the Planes of Convergence through the log diameters.

The dihedral angles between the Roof planes and planes of Convergence, 90-C5, can be calculated using the formula: (a, b) = arcos a  b) / ab

Given values for R1 and C5, the simpler trigonometric equation cos SS = cos R1 cos C5 solves the Pitch angles of the Roof planes with respect to the Inclined deck. Angles DD and P2 may be solved; these angles must be equal at matching faces and edges.

For a Compound joint to be feasible:

All R1 (Bevel angles) must be equal.

All DD (Miter angles) at matching faces must be equal.

The sum of the C5 angles about a ridge line is constant.

The sum of the P2 angles between ridges is constant.

All Ridge vector endpoints on the Inclined deck must lie on a circle.

# Text boxes

Ridge Vector

i

Plumb Line

Common Plane: mj

8/12 RAFTERS

Rafter Plane: nm

### BEAMS

Beam Plane: ji

Common Plane: in

Ridge Vector

j

m

n

## Plane of

Convergence thru Log Diameter

Ridge Vector

Convergence Vector: r

Ridge Vector

COMPOUND JOINT GEOMETRY:

The vertices of the polygon created by the inclined deck lie on the base of a right circular cone. In this case the polygon is a quadrilateral, therefore the opposite angles are supplementary.

Corollary: Since any triangle may be circumscribed, three members  always converge.

Convergence vector, r, lies on the altitude of the cone, and meets the Ridge vectors at the vertex. The Ridge vectors are of equal magnitude.

Rafter Plane: nm

n

(0, -.83205, -.55470)

8/12 RAFTER

8/12 RAFTER

Beam Plane: ji

Common Plane: mj

Common Plane: in

j

(0, 1, 0)

(1, 0, 0)

i

m  (-.83205, 0, -.55470)

33.69007

.83205

.55470

1

8/12 RAFTER

CO-ORDINATES

(1.01624, 1.01624, -3.35641)

r

(a, b) means the angle between vectors a and b, solved using the equation:

(a, b) = arcos a  b) / ab

r = a x b may be evaluated using the determinants of the matrices:

1	0	0

xa	ya	za

xb	yb	zb

0	1	0

xa	ya	za

xb	yb	zb

0	0	1

xa	ya	za

xb	yb	zb

xr =

yr =

zr =

#### All R1 angles at feet

= 16.161

#### ji, Beam plane

mj, Common plane

nm, Rafter plane

in, Common plane

#### ri,  Beam diameter

rj,  Beam diameter

rm,  Rafter diameter

rn,  Rafter diameter

Dihedral angle:

(ji, ri) = 73.15495

(ji, rj) = 73.15495

(mj, rj) = 73.15498

(mj, rm) = 73.15498

Dihedral angle:

(nm, rm) = 77.82788

(nm, rn) = 77.82788

(in, rn) = 73.15498

(in, ri) = 73.15498

C5

16.845

16.845

16.845

16.845

C5

12.172

12.172

16.845

16.845

BEAM

BEAM