HIP / VALLEY SQUARE CUT ANGLES:

Extracting kernels from the “stick”:

HIP / VALLEY SQUARE CUT ANGLES:

Valley Foot meets Main Common Rafter

HIP / VALLEY SQUARE CUT ANGLES:

### Valley Peak meets Main Purlin

HIP / VALLEY SQUARE CUT ANGLES:

### Valley Peak meets Main Purlin

W = 90 Degrees

# Text boxes

Main Purlin

Main Common Rafter

Valley Peak

Valley Peak meets Main Purlin

Valley Foot meets Main Common Rafter

Acute angles are created by the compound angle cuts where the Valley Peak meets Main Purlin and Valley Foot meets Main Common Rafter.

The process of extracting kernels to obtain a set of angles is the same as used to solve the square cuts for Purlin meets Valley and Rafter meets Valley. The appropriate square cut lines, with their planes, are moved until they are superimposed on the corresponding parallel line on the Compound face. This creates a false miter or bevel line, and dihedral angle, on one of the faces, from which a kernel describing the relationships between the angles may be extracted.

Since the angles concerned are at the bottom and side faces of the Valley rafter, for the sake of clarity, backing angle cuts and other planes on the final product are not depicted.

Plan

The section of the Valley rafter is removed to accommodate the adjacent Valley; the intercept of this cut and the square cut on the bottom face produces another kernel.

## R4B

R4P

180-(R4P+R4B)

NOTE : Regardless of the value of Total Deck Angle,W, the square cut is still perpendicular to the Compound face, which follows the side face of the Main Common rafter.

A kernel which describes R6P :

tan R6P = tanA5P sinR4P

## Dihedral angle  =

## 90-A5P

## Dihedral angle  =

## 90-DD

The same kernel as Valley Peak meets Header. Since the cut is square to the side face of the Main Common Rafter, the angles follow the plumb, parallel plane equivalent to a Header. If W = 90 degrees, the equal Adjacent peak values may be substituted.

Miter remains constant

A5P

90-R1

90+R1-R6P

90-R1

Bevel remains constant

90-R1

Triangle created on top face

Triangle created on side face

## Dihedral angle = A5P

## Dihedral angle =

## 90-R6PBV

Remains constant

R4P

VC

#### R6P

90-A5B

R4P

R6P

#### R6P

90-R1

## Dihedral angle = 90-A5B

Remains constant

R4P

#### R4P

90-R5B

R4B

90-R1

## Dihedral angle = DD

#### R4B

90-R2

Triangle created on side face

90-R3

R7

90-R2

90+R2-R7

90-R3

R7

#### Dihedral angle = C2

Dihedral angle  = 90-R7BV

# Miter remains constant

90-R3

R7

C2

VP

tanR7 = tanC2 cosR3

Valley peak

A kernel is created where the Valley  Peak meets Main Purlin square cut intercepts the Valley Peak meets Valley Peak cut.

General Model of Valley Angles:

Main side. Refer to appropriate section for angle details.

Planes of interest:

Kernel extracted from General Model

Plane parallel to Valley meets Valley plane

Bottom face of Valley

Plane of Purlin at right angles to Roof plane

Kernel extracted from kernel, and re-drawn in standard position. This model clearly shows that the required angle is to calculate Q4 is R4P.

90-P3

90-P6

90-C2

Dihedral angle  = 90-A5P

90-Q4

## R3

Dihedral angle = 90-C1

Bottom face of Valley rafter:

Angle details

Q4 = R4Pm-R3

= R4Ba-R3

Q4

R4Ba = R4Pm only if W = 90 Degrees

Angles R6P, R7, and Q4 are not strictly necessary to complete the square cut; they are projections of dihedral angles A5 and C2 respectively (much as P3 and P6 are projections of C5), and will occur “naturally” on the side faces of members after making the cut. These angles are required for developments if a 3-D model of a joint is desired.

90-R3

Dihedral angle

= 90-C2

R4Ba